## Slide 1: Final Project: Radiation Mapping
Elliott Caton, Augustina Jolly, Vivian Smart-Stewart

## Slide 2: Thesis
Urban terrain alters the amount of radiation detected from natural geographic sources of radiation.
Variable Considerations:
Time of collection
Weather variation
Human presence

## Slide 3: Collection Procedure
Ensure proper sensor setup and connections
Test of the detection cycle indoors
  Sensor functions
  Data Storage Locations
  File Types (2 CSV files)
Set collection intervals
  15 minutes total
  2 second intervals
Repeat collection at all 7 location
  Repeat if errors occur

## Slide 4: Map of Data Points
Etcheverry Breezeway
College of Chemistry Latimer Hall
McLaughlin Patio, Construction site
Gateway Construction Site
Foothill Parking lot and Amphitheatre Construction Site
Faculty Club
Stu Gordon Stadium

## Slide 5: Analysis Procedure
Remove outliers due to P/T/H sensor
  410 data points
Determine statistical values and graph
  Mean and standard deviation
  Histograms of counts
  Time series plots of air quality
Plot spectrum data

## Slide 6: Location 1: Etcheverry Breezeway
Counts: 38.4 4.2
PM 10: 2.3 1.1
Temperature: 27.5 0.4
Factors: buildings, people

## Slide 7: Location 2: College of Chemistry, Latimer Hall
Counts: 48.3 4.6
PM 10: 2.6 1.0
Temperature: 25.8 0.2
Factors: buildings

## Slide 8: Location 3: McLaughlin Patio, Construction Site
Counts: 39.9 4.1
PM 10: 3.2 0.8
Temperature: 28.1 0.1
Factors: buildings, construction, people

## Slide 9: Location 4: Gateway Construction Site
Counts: 47.8 4.6
PM 10: 1.5 1.0
Temperature: 23.0 0.4
Factors: construction

## Slide 10: Location 5: Foothill Parking Lot and Amphitheatre Construction
Counts: 39.9 4.1
PM 10: 2.2 1.1
Temperature: 26.8 0.2
Factors: construction

## Slide 11: Location 6: Faculty Club
Counts: 34.8 4.3
PM 10: 2.6 1.2
Temperature: 27.5 0.2
Factors:

## Slide 12: Location 7: Stu Gordon Stadium
Counts: 32.9 4.2
PM 10: 1.1 0.8
Temperature: 26.5 1.2
Factors:

## Slide 13: Irregular Data
Taking data on different days affected air quality

## Slide 14: Conclusions
Active construction correlates to more counts