## Slide 1: Final Project: Radiation Mapping
Elliott Caton, Agustina Jolly, Vivian Smart-Stewart
Spring 2024

## Slide 2: Thesis
Urban terrain alters the amount of radiation detected from natural geographic sources of radiation.
Variable Considerations:
Time of collection
Weather variation
Human presence

## Slide 3: Collection Procedure
Ensure proper sensor setup and connections
Test of the detection cycle indoors
  Sensor functions
  Data Storage Locations
  File Types (2 CSV files)
Set collection intervals
  15 minutes total
  2 second intervals
Repeat collection at all 7 locations
  Repeat if errors occur

## Slide 4: Map of Data Points
Etcheverry Breezeway
College of Chemistry Latimer Hall
McLaughlin Patio, Construction site
Gateway Construction Site
Foothill Parking lot and Amphitheatre Construction Site
Faculty Club
Stu Gordon Stadium

## Slide 5: Analysis Procedure
Remove outliers due to P/T/H sensor
  410 data points
Determine statistical values and graph
  Mean and standard deviation
  Histograms of counts
  Time series plots of air quality
Plot spectrum data
  Determine significant peaks
  Rebin data to smoothen out noise
  Correlate channels with energy

## Slide 6: Location 1: Etcheverry Breezeway
Counts: 38.4 4.2
PM 10: 2.3 1.1
Temperature: 27.5 0.4
Factors: buildings, people

## Slide 7
K-40 1460 keV

## Slide 8: Location 2: College of Chemistry, Latimer Hall
Counts: 48.3 4.6
PM 10: 2.6 1.0
Temperature: 25.8 0.2
Factors: buildings

## Slide 9
~ 600 keV

## Slide 10: Location 3: McLaughlin Patio, Construction Site
Counts: 39.3 4.1
PM 10: 3.2 0.8
Temperature: 28.1 0.1
Factors: construction, people

## Slide 12: Location 4: Gateway Construction Site
Counts: 47.8 4.6
PM 10: 1.5 1.0
Temperature: 23.0 0.4
Factors: buildings, construction

## Slide 14: Location 5: Foothill Parking Lot and Amphitheatre Construction
Counts: 39.9 4.1
PM 10: 2.2 1.1
Temperature: 26.8 0.2
Factors: construction

## Slide 16: Location 6: Faculty Club
Counts: 34.8 4.3
PM 10: 2.6 1.2
Temperature: 27.5 0.2
Factors: low density of people

## Slide 18: Location 7: Stu Gordon Stadium
Counts: 32.9 4.2
PM 10: 1.1 0.8
Temperature: 26.5 1.2
Factors: air quality, terrain

## Slide 20: Irregular Data
Taking data on different days affected air quality
Need more data (longer intervals, multiple days) to notice statistically significant variations

## Slide 21: Spectrum range comparisons
~ 2.75 keV / channel based off knowing K-40 has a known peak at 1460 keV, roughly on channel 520

## Slide 22: Conclusions
Active construction, more people, and nearby buildings correlate to more counts